## Slide 1: Chapter 5 Network Layer: The Control Plane

## Slide 2: Chapter 5 Network Layer
our goals:
understand principles behind network control plane:
  traditional routing algorithms
  SDN controlllers
  Internet Control Message Protocol
  network management
and their instantiation, implementation in the Internet
  OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP
- The Control Plane

## Slide 3
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 4
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 5: Network-layer functions
forwarding: move packets from router's input to appropriate router output
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination
5.1 introduction

## Slide 6
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane
5.1 introduction

## Slide 7
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA
5.1 introduction

## Slide 8
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 9: Routing protocols
Routing protocol goal: determine "good" paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
"good": least "cost", "fastest", "least congested"
routing: a "top-10" networking challenge!
5.2 routing protocols

## Slide 10: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections
5.2 routing protocols

## Slide 11: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x') = cost of link (x,x')
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path
5.2 routing protocols

## Slide 12: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
"link state" algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
"distance vector" algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes
5.2 routing protocols

## Slide 13
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 14: A link-state routing algorithm
Dijkstra's algorithm
net topology, link costs known to all nodes
  accomplished via "link state broadcast"
  all nodes have same info
computes least cost paths from one node ("source") to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.'s
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known
5.2 routing protocols

## Slide 15: Dijsktra's algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
5.2 routing protocols

## Slide 16: Dijsktra's algorithm
5.2 routing protocols
Dijkstra 最短路径算法
  G=(V,E)是一个带权有向图，V分成两组S和T，V=S U T。S为已求出最短路径的顶点集合。初始S中只有一个源点v，以后每求得一条最短路径 , 就将加入S中，直到S=V。从T中找出到v最短路径的点p依次加入S中。在加入的过程中，保持从v到S中各顶点的最短路径长度不大于从v到T的最短路径长度。每个顶点对应一个距离，S中的顶点的距离就是从v到此顶点的最短路径长度，T中顶点t的距离，是从v到t只包括S中的顶点为中间顶点的当前最短路径长度。流程：
  1) 初始时，S＝{v}，v的距离为0。T=V-{v}，若v与T中顶点u有边，则<u,v>正常有权值，若u不是v的邻接点，则<u,v>权值为∞
  2) 从T中选取一个距离v最小的顶点k加入S中(该距离就是v到k的最短路径长度)
  3) 以k为中间点，修改T中各顶点的距离；若从源点v到顶点u的距离（经过顶点k）比原来距离（不经过顶点k）短，则修改顶点u的距离值为v到k的距离加上k到u的距离(k到u的边的权)，修改后的距离值的顶点k的距离加上边上的权
  4) 重复2)和3)直到所有顶点都包含在S中

## Slide 17: Dijsktra's algorithm
5.2 routing protocols
Dijkstra 最短路径算法
  G=(V,E)是一个带权有向图，V分成两组S和T，V=S U T。S为已求出最短路径的顶点集合。初始S中只有一个源点v，以后每求得一条最短路径 , 就将加入S中，直到S=V。从T中找出到v最短路径的点p依次加入S中。在加入的过程中，保持从v到S中各顶点的最短路径长度不大于从v到T的最短路径长度。每个顶点对应一个距离，S中的顶点的距离就是从v到此顶点的最短路径长度，T中顶点t的距离，是从v到t只包括S中的顶点为中间顶点的当前最短路径长度。流程：
  1) 初始时，S＝{v}，v的距离为0。T=V-{v}，若v与T中顶点u有边，则<u,v>正常有权值，若u不是v的邻接点，则<u,v>权值为∞
  2) 从T中选取一个距离v最小的顶点k加入S中(该距离就是v到k的最短路径长度)
  3) 以k为中间点，修改T中各顶点的距离；若从源点v到顶点u的距离（经过顶点k）比原来距离（不经过顶点k）短，则修改顶点u的距离值为v到k的距离加上k到u的距离(k到u的边的权)，修改后的距离值的顶点k的距离加上边上的权
  4) 重复2)和3)直到所有顶点都包含在S中

## Slide 18
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra's algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz
5.2 routing protocols

## Slide 19: Dijkstra's algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
5.2 routing protocols

## Slide 20: Dijkstra's algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:
5.2 routing protocols

## Slide 21: Dijkstra's algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:
e.g., support link cost equals amount of carried traffic:
A
D
C
B
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
5.2 routing protocols
1

## Slide 22
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 23: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y
5.2 routing protocols

## Slide 24: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:
5.2 routing protocols

## Slide 25: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors' distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
5.2 routing protocols

## Slide 26: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
5.2 routing protocols

## Slide 27: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:
5.2 routing protocols

## Slide 28
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
5.2 routing protocols

## Slide 29
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
5.2 routing protocols

## Slide 30: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
"good
news
travels
fast"
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z's update, updates its distance table. y's least costs do not change, so y does not send a message to z.
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
5.2 routing protocols

## Slide 31: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - "count to infinity" problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
5.2 routing protocols
algorithm
continues
on!

## Slide 32: Distance vector: link cost changes
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z's) distance to X is infinite (so Y won't route to X via Z)
will this completely solve count to infinity problem?
5.2 routing protocols
algorithm
terminates

## Slide 33: Distance vector: link cost changes
5.2 routing protocols
https://en.wikipedia.org/wiki/Distance-vector_routing_protocol#Count-to-infinity_problem
Counting to Infinity Problem Solutions
Set infinity = “some small integer” (e.g. 16). Stop when count = 16.
Split Horizon: Because C received lowest cost path from B, it does not advertise cost to B
poison reverse: C advertises infinity to B
There are many problems with (and fixes for) the Bellman-Ford algorithm.

## Slide 34: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - "count to infinity" problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z's) distance to X is infinite (so Y won't route to X via Z)
will this completely solve count to infinity problem?
5.2 routing protocols
导致无穷计算问题的原因是把从对方获知的，但在对方已不再有效的信息当成有效信息再传送给对方，使对方当成有效信息使用。

## Slide 35: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node's table used by others
    error propagate thru network
5.2 routing protocols

## Slide 36
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 37: Making routing scalable
scale: with billions of destinations:
can't store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network "flat"
… not true in practice
5.3 OSPF

## Slide 38: Internet approach to scalable routing
aggregate routers into regions known as "autonomous systems" (AS) (a.k.a. "domains")
inter-AS routing
routing among AS'es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS ("network")
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at "edge" of its own AS, has link(s) to router(s) in other AS'es
5.3 OSPF

## Slide 39: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations
5.3 OSPF

## Slide 40: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
5.3 OSPF

## Slide 41: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)
5.3 OSPF

## Slide 42: OSPF (Open Shortest Path First)
"open": publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra's algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link
IS-IS routing protocol: nearly identical to OSPF
5.3 OSPF
Intermediate System to Intermediate System
https://en.wikipedia.org/wiki/IS-IS
Notes: IS-IS: Layer 2 protocol
OSPF: Layer 3 protocol

## Slide 43: OSPF "advanced" features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.
5.3 OSPF
Notes: Terms of Service 服务条款

## Slide 44: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
5.3 OSPF

## Slide 45: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: "summarize" distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS'es.
5.3 OSPF

## Slide 46
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 47: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  "glue that holds the Internet together"
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine "good" routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: "I am here"
5.4 BGP

## Slide 48: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protools
5.4 BGP

## Slide 49: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers ("peers") exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a "path vector" protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X
5.4 BGP

## Slide 50: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = "route"
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes
5.4 BGP

## Slide 51: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
5.4 BGP

## Slide 52: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP
5.4 BGP

## Slide 53: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
5.4 BGP

## Slide 54: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: "path to X goes through 1c"
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d
5.4 BGP

## Slide 55: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: "path to X goes through 1c"
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2
5.4 BGP

## Slide 56: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
5.4 BGP

## Slide 57: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don't worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263
5.4 BGP

## Slide 58: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no "revenue" for routing CBAw, since none of C, A, w are B's customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
5.4 BGP

## Slide 59: BGP: achieving policy via advertisements
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
5.4 BGP

## Slide 60: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance
5.4 BGP

## Slide 61
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 62
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different "middleboxes" for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane
5.5 The SDN control plane

## Slide 63
Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane
5.5 The SDN control plane

## Slide 64
data
plane
control
plane
Recall: logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA
5.5 The SDN control plane

## Slide 65
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows "programming" routers
  centralized "programming" easier: compute tables centrally and distribute
  distributed "programming: more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane
5.5 The SDN control plane

## Slide 66: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
5.5 The SDN control plane

## Slide 67: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control "knobs": wrong!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
5.5 The SDN control plane
Notes: Note: implicit assumption here: destination based forwarding

## Slide 68: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can't do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
5.5 The SDN control plane
Notes: Note: implicit assumption here: destination based forwarding

## Slide 69: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route orange and red traffic differently?
A: can't do it (with destination based forwarding, and LS, DV routing)
5.5 The SDN control plane
Notes: Note: implicit assumption here: destination based forwarding

## Slide 70
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized" flow-based" forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance
5.5 The SDN control plane

## Slide 71
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN control plane

## Slide 72
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications "above" via northbound API
interacts with network switches "below" via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN control plane

## Slide 73
SDN perspective: control applications
network-control apps:
"brains" of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN control plane

## Slide 74
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API
5.5 The SDN control plane

## Slide 75: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
OpenFlow Controller
5.5 The SDN control plane
port # 6653

## Slide 76: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller
5.5 The SDN control plane

## Slide 77: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don't "program" switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller
5.5 The SDN control plane

## Slide 78
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra's routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra's routing algorithm access network graph info, link state info in controller, computes new routes
4
5.5 The SDN control plane

## Slide 79
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6
5.5 The SDN control plane

## Slide 80
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight (ODL) controller
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services
5.5 The SDN control plane
https://wiki.opendaylight.org/view/OpenDaylight_Controller:REST_Reference_and_Authentication
Neon
Notes: Neon: Version 10

## Slide 81
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS controller
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling
5.5 The SDN control plane

## Slide 82
SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: "baked in" from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling
5.5 The SDN control plane

## Slide 83
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 84: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer "above" IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
5.6 ICMP
Notes: source quench: 源抑制

## Slide 85: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number (e.g. 80)
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP "port unreachable" message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
5.6 ICMP

## Slide 86
5.1 introduction
5.2 routing protocols
  link state
  distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
Chapter 5 Network Layer
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
- The Control Plane
Network Layer - the control plane
Notes: SDN: software defined network

## Slide 87: What is network management?
autonomous systems (aka "network"): 1000s of interacting hardware/software components
other complex systems requiring monitoring, control:
  jet airplane
  nuclear power plant
  others?
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."
5.7 SNMP
Notes: poll: 轮询、挂起到队列

## Slide 88: Infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
network
management
protocol
managed device
agent
data
agent
data
agent
data
5.7 SNMP

## Slide 89: SNMP protocol
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response
5.7 SNMP
Notes: trap message: 陷阱报文，例如链路接口的启动与关闭时发送非请求报文

## Slide 90: SNMP protocol: message types
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: "get me data"
(data instance, next data in list, block of data)
Message type
Function
InformRequest
manager-to-manager: here's MIB value
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to
Request
Trap
Agent-to-manager: inform manager
of exceptional event
5.7 SNMP
SNMP operates in the application layer
SNMP messages are transported via UDP
protocol data unit — PDU

## Slide 91: SNMP protocol: message formats
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Get/set header
Variables to get/set
Trap header
Trap info
SNMP PDU
More on network management: see earlier editions of text!
5.7 SNMP
PDU format
Notes: PDU: Protocol Data Unit

## Slide 92
Chapter 5 summary
Network Layer - the control plane
we've learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
network management
next stop: link layer!

## Slide 93
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
The Internet Hourglass
link
layer
ethernet
802.11
SONET
ATM
Network Layer - the control plane

## Slide 94: Homework
每章选做5道，该章教学完成后一周内提交，可以提前提交
Network Layer - the control plane